## Slide 1: ECE/CS 584: Verification of Embedded Computing Systems Model Checking Timed Automata
Sayan Mitra
Lecture 09

## Slide 2: Reachability analysis: Integer Timed Automaton
Sayan Mitra
Verifying cyberphysical systems
mitras@illinois.edu

## Slide 3: This course so far
A modeling framework
  Discrete and continuous dynamics
  Compositional (modular) modeling
General proof techniques for proving invariants

## Slide 4: Next
Focus on specific classes of Hybrid Automata for which safety properties (invariants) can be verified completely automatically
  Alur-Dill’s Timed Automata[1] (Today)
  Rectangular initializaed hybrid automata
  Linear hybrid automata
  …
Later we will look at other types of properties like stability, liveness, etc.
We will introduce notions of abstractions and invariance are still going to be important
[1] Rajeev Alur et al. The Algorithmic Analysis ofHybrid Systems. Theoretical Computer Science, colume 138, pages 3-34, 1995.

## Slide 5: Today
Algorithmic analysis of (Alur-Dill’s) Timed Automata[1]
  A restricted class of what we call hybrid automata in this course with only clock variables
[1] Rajeev Alur and David L. Dill. A theory of timed automata. Theoretical Computer Science, 126:183-235, 1994.

## Slide 6: Clocks and Clock Constraints
A clock variable x is a continuous (analog) variable of type real such that along any trajectory of x, for all t .
For a set X of clock variables, the set (X) of integral clock constraints are expressions defined by the syntax:
  g ::= x
  where
Examples: x = 10; x [2, 5); true are valid clock constraints
What do clock constraints look like?
Semantics of clock constraints

## Slide 7: Integral Timed Automata
Definition. A integral timed automaton is a HIOA where
  V = X , where is a set of n clocks and is a discrete state variable of finite type Ł
  A is a finite set
  is a set of transitions such that
    The guards are described by clock constraings
    implies either or
  set of clock trajectories for the clock variables in X

## Slide 8: Example: Light switch
Math Formulation
automaton Switch
  variables
  internal x, y:Real := 0, loc: {on,off} := off
  transitions
  internal push
pre x 2
eff if loc = on then x := 0
else x,y := 0; loc := off
  internal pop
pre y = 15 /\ loc = off
eff x := 0
  trajectories
invariant loc = off => y 15
evolve d(x) = 1; d(y) = 1
Description
Switch can be turned on whenever at least 2 time units have elapsed since the last turn on. Switches off automatically 15 time units after the last on.

## Slide 9: Control State (Location) Reachability Problem
Given an ITA, check if a particular (discrete) control state is reachable from the initial states
Why is control state reachability (CSR) good enough?
This problem is decidable [Alur Dill]
Key idea:
  Construct a finite automaton that is a time-abstract bisimilar to the ITA (behaves identically with respect to control state reachability)
  Check reachability of FSM

## Slide 10: An equivalence relation with a finite quotient
Under what conditions do two states x1 and x2 of the automaton behave identically with respect to control state reachability (CSR)?
  When do they satisfy the same set of clock constraints?
  When would they continue to satisfy the same set of clock constraints?
x1.and
x1 and x2 satisfy the same set of clock constraints
  For each clock int(x1.) = int(x2.) or int(x1.and int(x2.. ( of )
  For each clock with x1., frac(x1.iff frac(x2.
  For any two clocks and with x1. and x1., frac(x1.) frac(x1.) iff frac(x2.) frac(x2.)
Lemma. This is a equivalence relation on val(V) the states of
The partition of val(V) induced by this relation is are called clock regions

## Slide 11: What do the clock regions look like?
Example of Two Clocks
X = {y,z}
= 2
= 3

## Slide 12: Complexity
Lemma. The number of clock regions is bounded by |X|! 2|X|.

## Slide 13: Region Automaton
ITA (clock constants) defines the clock regions
Now we add the “appropriate transitions” between the regions to create a finite automaton which gives a visits the same set of states (but timing information is lost) ITA with respect to control state reachability
  Time successors: Consider two clock regions , we say that is a time successor of if there exits a trajectory of ITA starting from that ends in ’
  Discrete transitions: Same as the ITA

## Slide 14: Time Successors
The clock regions in blue are time successors of the clock region in red.

## Slide 15: Example 1: Region Automata
ITA
Corresponding FA

## Slide 16: Example 2
ITA
Clock Regions

## Slide 17
|X|! 2|X|
Corresponding FA
Drastically increasing with the number of clocks

## Slide 18: Summary
ITA: (very) Restricted class of hybrid automata
  Clocks, integer constraints
  No clock comparison, linear
Control state reachability
Alur-Dill’s algorithm
  Construct finite bisimulation (region automaton)
  Idea is to lump together states that behave similarly and reduce the size of the model
UPPAAL model checker based on similar model of timed automata